## Slide 1: BikewaySim: Using impedance to estimate improvement in perceived safety from new cycling infrastructure
Reid Passmore, Dr. Kari E. Watkins, Dr. Randall Guensler
SETT Conference
June, 2nd, 2022

## Slide 2: Need for better cycling infrastructure in the U.S.
Real and perceived danger imposed on cyclists by cars when sharing the same space is a major deterrent to cycling in the U.S.
Street view images from Google Maps

## Slide 3: We already have good bike design guidelines
But where and what kind of infrastructure to place to best increase the perceived safety of cycling?

## Slide 4: Introducing BikewaySim
What:
  Python based shortest path calculator
  Finds least impedance path for cycling trips for any origin/destination pair
How:
  Uses Dijkstra's algorithm to find shortest path using impedance
  Uses link impedance to model cyclist’s preferences for road attributes
Why:
  To evaluate how new cycling facilities change aggregate impedance
    To prioritize infrastructure that increases perceived safety
  To provide suggested routes
Notes: Animate?

## Slide 5: Link Impedance
Typically represented by travel time, not sufficient for cycling
Cyclists’ show preferences for certain road attributes:
  Bike infrastructure, slow speed streets, traffic signals
And avoidance of other attributes:
  Turns, hills, busy roads, distance
Hood, J., E. Sall, and B. Charlton. A GPS-based bicycle route choice model for San Francisco. Transportation Letters, 2013.
Fitch, D. T., and S. L. Handy. Road environments and bicyclist route choice: The cases of Davis and San Francisco, CA. Journal of Transport Geography, 2020.
Menghini, G., N. Carrasco, Schüssler, and K. Axhausen. Route choice of cyclists in Zurich. Transportation Research Part A, 2010.

## Slide 6: Desired impedance function form
Where:
: the impedance to traverse link i in units of time
: length of link i
: assumed average cyclist speed
: attribute specific impedance coefficient, k, for link i
: link attribute, k, for link i
Path/route impedance = sum of link impedances

## Slide 7: Desired impedance function form
Where:
: the impedance to traverse link i in units of time
: length of link i
: assumed average cyclist speed
: attribute specific impedance coefficient, k, for link i
: link attribute, k, for link i
Path/route impedance = sum of link impedances

## Slide 8: How to calibrate impedance functions?
Network Data with Attribute Data
Cycling Data
Observed Cyclists:
Bicycle Volume Counts
GPS Trajectory Data
Potential Cyclists:
Stated Preferences for Cycling Facilities
Calibration Process
Impedance Functions

## Slide 9: How to calibrate impedance functions?
Network Data with Attribute Data
Cycling Data
Observed Cyclists:
Bicycle Volume Counts
GPS Trajectory Data
Potential Cyclists:
Stated Preferences for Cycling Facilities

## Slide 10: How to calibrate impedance functions?
Network Data with Attribute Data
Cycling Data
Observed Cyclists:
Bicycle Volume Counts
GPS Trajectory Data
Potential Cyclists:
Stated Preferences for Cycling Facilities
Basemap from CartoDB

## Slide 11: How to calibrate impedance functions?
Network Data with Attribute Data
Cycling Data
Observed Cyclists:
Bicycle Volume Counts
GPS Trajectory Data
Potential Cyclists:
Stated Preferences for Cycling Facilities
Survey from National Academies of Sciences, Engineering, and Medicine 2020. Bicyclist Facility Preferences and Effects on Increasing Bicycle Trips. Washington, DC: The National Academies Press. https://doi.org/10.17226/25792

## Slide 12: How to calibrate impedance functions?
Network Data with Attribute Data
Cycling Data
Observed Cyclists:
Bicycle Volume Counts
GPS Trajectory Data
Potential Cyclists:
Stated Preferences for Cycling Facilities
Signalization
# of traffic lanes, speed limit, traffic volume
Street view images from Google Maps
Bike facility type

## Slide 13: How to calibrate impedance functions?
Network Data with Attribute Data
Cycling Data
Observed Cyclists:
Bicycle Volume Counts
GPS Trajectory Data
Potential Cyclists:
Stated Preferences for Cycling Facilities
One way restriction
On-street parking
Street view images from Google Maps

## Slide 14: How to calibrate impedance functions?
Network Data with Attribute Data
Cycling Data
Observed Cyclists:
Bicycle Volume Counts
GPS Trajectory Data
Potential Cyclists:
Stated Preferences for Cycling Facilities
Hills

## Slide 15: How to calibrate impedance functions?
Network Data with Attribute Data
Cycling Data
Observed Cyclists:
Bicycle Volume Counts
GPS Trajectory Data
Potential Cyclists:
Stated Preferences for Cycling Facilities
Multi-use paths
Cycletracks

## Slide 16: How to calibrate impedance functions?
Network Data with Attribute Data
Cycling Data
Observed Cyclists:
Bicycle Volume Counts
GPS Trajectory Data
Potential Cyclists:
Stated Preferences for Cycling Facilities
Need network data with attributes
Municipal data is limited for our study area
For this project we looked at three sources:
  ABM: Our MPOs activity based model network
  HERE: Licensed data on roads from HERE
  OSM: OpenStreetMap

## Slide 17: How to calibrate impedance functions?
Network Data with Attribute Data
Cycling Data
Observed Cyclists:
Bicycle Volume Counts
GPS Trajectory Data
Potential Cyclists:
Stated Preferences for Cycling Facilities
Notes: Pull off greater atlanta map to the side to fill in white space

## Slide 18: How to calibrate impedance functions?
Network Data with Attribute Data
Cycling Data
Observed Cyclists:
Bicycle Volume Counts
GPS Trajectory Data
Potential Cyclists:
Stated Preferences for Cycling Facilities
Network Type | Network Name | Number of Links | Number of Nodes | Total Length (mi.)
Total | ABM | 2,542 | 2,065 | 182
 | HERE | 12,286 | 9,535 | 401
 | OSM | 24,198 | 17,029 | 627
ABM
HERE
OSM
Notes: Going to just have maps of the network and the overall counts because they say pretty much the same thing.

## Slide 19: How to calibrate impedance functions?
Network Data with Attribute Data
Cycling Data
Observed Cyclists:
Bicycle Volume Counts
GPS Trajectory Data
Potential Cyclists:
Stated Preferences for Cycling Facilities
Attribute | ABM | HERE | OSM
Bicycle Facilities | - | - | ◑
Bicycle Facility Width | - | - | -
Bicycle Facility Blockage | - | - | -
Bicycle Traffic Volume | - | - | -
Sidewalks | - | - | ◑
Sidewalk Width | - | - | -
Number of Lanes | ● | ● | ◑
Travel Lane Width | - | - | -
Shoulder Width | - | - | -
Traffic Volume | ● | - | -
Directions Allowed | ● | ● | ◑
Road Classification | ● | ● | ●
Speed Limit | ● | ● | ◑
Observed Speed Limit | ● | - | -
Median Presence | ● | ● | -
On Street Parking | - | - | ○
Road Grade/Slope | - | - | -
Bridge/Tunnel | - | ● | ○
Legend:
‘-‘: Attribute not available
‘○’: Less than 1% data available
‘◑’: 1%-50% data available
‘●’: > 50% of data available
Notes: Maybe take out one of these and make sure to streamline

## Slide 20: How to calibrate impedance functions?
Network Data with Attribute Data
Cycling Data
Observed Cyclists:
Bicycle Volume Counts
GPS Trajectory Data
Potential Cyclists:
Stated Preferences for Cycling Facilities
Attribute | ABM | HERE | OSM
Bicycle Facilities | - | - | ◑
Bicycle Facility Width | - | - | -
Bicycle Facility Blockage | - | - | -
Bicycle Traffic Volume | - | - | -
Sidewalks | - | - | ◑
Sidewalk Width | - | - | -
Number of Lanes | ● | ● | ◑
Travel Lane Width | - | - | -
Shoulder Width | - | - | -
Traffic Volume | ● | - | -
Directions Allowed | ● | ● | ◑
Road Classification | ● | ● | ●
Speed Limit | ● | ● | ◑
Observed Speed Limit | ● | - | -
Median Presence | ● | ● | -
On Street Parking | - | - | ○
Road Grade/Slope | - | - | -
Bridge/Tunnel | - | ● | ○
Legend:
‘-‘: Attribute not available
‘○’: Less than 1% data available
‘◑’: 1%-50% data available
‘●’: > 50% of data available
Notes: Need to fix circle sizes; rephrase osm completion

## Slide 21: How to calibrate impedance functions?
Network Data with Attribute Data
Cycling Data
Observed Cyclists:
Bicycle Volume Counts
GPS Trajectory Data
Potential Cyclists:
Stated Preferences for Cycling Facilities
Attribute | ABM | HERE | OSM
Bicycle Facilities | - | - | ◑
Bicycle Facility Width | - | - | -
Bicycle Facility Blockage | - | - | -
Bicycle Traffic Volume | - | - | -
Sidewalks | - | - | ◑
Sidewalk Width | - | - | -
Number of Lanes | ● | ● | ◑
Travel Lane Width | - | - | -
Shoulder Width | - | - | -
Traffic Volume | ● | - | -
Directions Allowed | ● | ● | ◑
Road Classification | ● | ● | ●
Speed Limit | ● | ● | ◑
Observed Speed Limit | ● | - | -
Median Presence | ● | ● | -
On Street Parking | - | - | ○
Road Grade/Slope | - | - | -
Bridge/Tunnel | - | ● | ○
Legend:
‘-‘: Attribute not available
‘○’: Less than 1% data available
‘◑’: 1%-50% data available
‘●’: > 50% of data available
Notes: Need to fix circle sizes; rephrase osm completion

## Slide 22: How to calibrate impedance functions?
Network Data with Attribute Data
Cycling Data
Observed Cyclists:
Bicycle Volume Counts
GPS Trajectory Data
Potential Cyclists:
Stated Preferences for Cycling Facilities
Attribute | ABM | HERE | OSM
Bicycle Facilities | - | - | ◑
Bicycle Facility Width | - | - | -
Bicycle Facility Blockage | - | - | -
Bicycle Traffic Volume | - | - | -
Sidewalks | - | - | ◑
Sidewalk Width | - | - | -
Number of Lanes | ● | ● | ◑
Travel Lane Width | - | - | -
Shoulder Width | - | - | -
Traffic Volume | ● | - | -
Directions Allowed | ● | ● | ◑
Road Classification | ● | ● | ●
Speed Limit | ● | ● | ◑
Observed Speed Limit | ● | - | -
Median Presence | ● | ● | -
On Street Parking | - | - | ○
Road Grade/Slope | - | - | -
Bridge/Tunnel | - | ● | ○
Legend:
‘-‘: Attribute not available
‘○’: Less than 1% data available
‘◑’: 1%-50% data available
‘●’: > 50% of data available
Notes: Need to fix circle sizes; rephrase osm completion

## Slide 23: How to calibrate impedance functions?
Network Data with Attribute Data
Cycling Data
Observed Cyclists:
Bicycle Volume Counts
GPS Trajectory Data
Potential Cyclists:
Stated Preferences for Cycling Facilities
ABM network has traffic volume and observed speed attributes
HERE has good overall attribute completion
OSM has more bike facility data and most link mileage
Need to combine networks
Notes: Change to plus plus equal

## Slide 24: How to calibrate impedance functions?
Network Data with Attribute Data
Cycling Data
Observed Cyclists:
Bicycle Volume Counts
GPS Trajectory Data
Potential Cyclists:
Stated Preferences for Cycling Facilities
Calibration Process
Three potential approaches:
  Marginal rates of substitution (MRS) or equivalent %∆ distance from existing route choice models
  Recursive logit models
  Route choice set generation with random coefficients
1) Broach J, J Dill, J Gliebe. Where do cyclists ride? A route choice model developed with revealed preference data. Transportation Research Part A: Policy and Practice. 2012; 46(10):1730-1740. doi:10.1016/j.tra.2012.07.005
2) Zimmermann M, T Mai, E Frejinger. Bike route choice modeling using GPS data without choice sets of paths. Transportation Research Part C: Emerging Technologies. 2017;75:183-196. doi:10.1016/j.trc.2016.12.009
3) Nassir N, Ziebarth J, Sall E, Zorn L. Choice Set Generation Algorithm Suitable for Measuring Route Choice Accessibility. Transportation Research Record. 2014;2430(1):170-181. doi:10.3141/2430-18
Notes: If anyone has experience with these I’d love to talk afterwards

## Slide 25: How to calibrate impedance functions?
Network Data with Attribute Data
Cycling Data
Observed Cyclists:
Bicycle Volume Counts
GPS Trajectory Data
Potential Cyclists:
Stated Preferences for Cycling Facilities
Calibration Process
Different approaches needed for these data
  Trajectory not known
  For stated preferences, there’s no spatial connection

## Slide 26: How to calibrate impedance functions?
Network Data with Attribute Data
Cycling Data
Observed Cyclists:
Bicycle Volume Counts
GPS Trajectory Data
Potential Cyclists:
Stated Preferences for Cycling Facilities
Calibration Process
Impedance Functions

## Slide 27: How to calibrate impedance functions?
Network Data with Attribute Data
Cycling Data
Observed Cyclists:
Bicycle Volume Counts
GPS Trajectory Data
Potential Cyclists:
Stated Preferences for Cycling Facilities
Calibration Process
Impedance Functions
More than one impedance function depending on user type

## Slide 28: Three uses of impedance functions
Bikeshed visualization
Preference based individual routing
Measuring change in aggregate impedance from network improvements
Notes: Do something with this slide

## Slide 29: Example impedance function
High stress streets are perceived as 4x the distance
Links with bike lanes viewed as 0.25x the distance

## Slide 30: Three uses of impedance functions
So if we have a 0.1 mile low-stress road with a bike lane:
Link is effectively shorter, less impedance to travel

## Slide 31
Study Area:
Atlanta, GA
Notes: Turn these back to miles

## Slide 32
Study Area:
Atlanta, GA
Midtown (dense, urban)
Georgia Tech
Virginia Highlands Neighborhood
(low-density, primarily single-family zoning)
Piedmont Park
BeltLine Multi-Use Path

## Slide 33
169 TAZs

## Slide 34
Street Network

## Slide 35
15 Minute Bikeshed

## Slide 36
15 Minute
Impedance Bikeshed
*regular 15 minute bikeshed not shown

## Slide 37
15 Minute Bikeshed

## Slide 38
Removed links

## Slide 39
New links

## Slide 40
15 Minute
Impedance Bikeshed
*regular 15 minute bikeshed not shown
BeltLine Multi-Use Path

## Slide 41
Individual Routing

## Slide 42
Individual Routing
Time

## Slide 43
Individual Routing
Impedance

## Slide 44
Least travel time path is not always the preferred path
Street view images from Google Maps

## Slide 45: Aggregated results using impedance
From all TAZs to all TAZs:
  28,392 OD pairs
Betweenness centrality
  # of trips using link for shortest path
Average impedance:
  15.2 minutes
Notes: Placeholder images until I redo these; convert text to table

## Slide 46: Network Improvement
Cycletrack added to 10th Street Northwest
10th Street is one of the few roads that cross I-75/85 interstate
Current Conditions:
Notes: Add streetview of current conditions

## Slide 47: Aggregated results after improvement
New average impedance
  15.1 minutes
Difference in impedance
  0.1 minutes
Can compare to other improvements and rank accordingly
Notes: Placeholder images until I redo these; convert text to table

## Slide 48: Aggregated results using impedance
Notes: Placeholder images until I redo these; convert text to table

## Slide 49: Conclusion
BikewaySim is an opensource shortest path calculator for cycling
BikewaySim can measure change in impedance from new infrastructure
  Planners and engineers can rank projects
Need calibration methods for:
  Trajectory data
  Aggregated data
  Stated preferences
BikewaySim Code Link:
Notes: This is my dissertation project, make sure to see feedback

## Slide 50: Questions/Suggestions?